## Slide 1
1
Year & Sem – III Year/ V sem
Subject – Electrical Machine Design
Subject Code – 5EE4-05
Unit – 1.3
Presented by – Mr. Atul Kulshrestha, Asstt Professor, EE
JAIPUR ENGINEERING COLLEGE AND RESEARCH CENTRE

## Slide 2
1
VISSION AND MISSION OF INSTITUTE
Vision of Jaipur Engineering College and Research Centre
To become a renowned centre of outcome based learning, and work towards academic, professional, cultural and social enrichment of the lives of individuals and communities.
Mission of Jaipur Engineering College and Research Centre
M1. Focus on evaluation of learning outcomes and motivate students to inculcate research aptitude by project based learning.
M2. Identify, based on informed perception of Indian, regional and global needs, areas of focus and provide platform to gain knowledge and solutions.
M3. Offer opportunities for interaction between academia and industry.
M4. Develop human potential to its fullest extent so that intellectually capable and imaginatively gifted leaders can emerge in a range of professions.

## Slide 3
1
VISSION AND MISSION OF DEPARTMENT
Vision of Department of Electrical Engineering
Electrical Engineering Department strives to be recognized globally for outcome based knowledge and to develop human potential to practice advance technology which contribute to society.
Mission of Department of Electrical Engineering
M1. To impart quality technical knowledge to the learners to make them globally competitive Electrical Engineers.
M2. To provide the learners ethical guidelines along with excellent academic environment for a long productive career.
M3. To promote industry-institute relationship.

## Slide 4
1
Materials for Electrical Machines
Conducting materials
Property of conducting material:
1. Low value of resistivity or high conductivity
2. Low value of temperature coefficient of resistance
3. High tensile strength
4. High melting point
5. High resistance to corrosion
6. Allow brazing, soldering or welding so that the joints are reliable
7. Highly malleable and ductile
8. Durable and cheap by cost

## Slide 5
1
Some of the properties of copper and aluminum are shown in the table
Sl. | Particulars | Copper |  | Aluminum
1 | Resistivity at 20 0C | 0.0172 ohm / m/ mm2 |  | 0.0269 ohm / m/ mm2
2 | Conductivity at 200C | 58.14 x 106S/m |  | 37.2 x 106 S/m
3 | Density at 200C | 8933 kg/m3 |  | 2689.9 Kg/m3
4 | Temperature coefficient (0-1000C) | 0.393 % per 0C |  | 0.4% per 0C
 | Explanation: If the temperature increases by 1oC, the resistance increases by 0.4% in case of aluminum |  |  | 
5 | Coefficient of linear expansion (0-100oC) |  | 16.8x10-6 per oC | 23.5 x10-6 per oC
For the same resistance and length, cross-sectional area of aluminum is 61% larger than that of the copper conductor and almost 50% lighter than copper.

## Slide 6
1
Magnetic materials
Property of magnetic material: The magnetic properties of a magnetic material depend on the orientation of the crystals of the material and decide the size of the machine or equipment for a given rating, excitation required, efficiency of operation etc.
The properties that a good magnetic material should possess are :
Low reluctance or should be highly permeable or should have a high value of relative permeability μr.
2. High saturation induction (to minimize weight and volume of iron parts)
3. High electrical resistivity so that the eddy EMF and the hence eddy current loss is less
4. Narrow hysteresis loop or low Coercivity so that hysteresis loss is less and efficiency of operation is high
5. A high curie point. (Above Curie point or temperature the material loses the magnetic property or becomes paramagnetic, that is effectively non-magnetic)
6. Should have a high value of energy product

## Slide 7: Some Magnetic materials
Material | Maximum permeability | Saturation magnetization | Coercivity | Curie temperature | Resistivity
 | μ x 10-3 | in Tesla | A/m | oC | Ωm x 108
3% Si grain oriented | 90 | 2 | 6-7 | 745 | 48
2.5% Si grain non -oriented | 8 | 2 | 40 | 745 | 44
<0.5% Si grain non oriented | 8 | 2.1 | 50-100 | 770 | 12
Low carbon iron | 3-10 | 2.1 | 50-120 | 770 | 12
78% Ni and iron | 250-400 | 0.8 | 1 | 350 | 40
50% Ni and iron | 100 | 1.5-1.6 | 10 | 530 | 60
Iron based Amorphous | 35-600 | 1.3-1.8 | 1.0-1.6 | 310-415 | 120-140

## Slide 8
1
Magnetic Materials
Magnetic materials can broadly be classified as Diamagnetic, Paramagnetic, Ferromagnetic, Antiferromagnetic and Ferrimagnetic materials. Only ferromagnetic materials have properties that are well suitable for electrical machines.
Ferromagnetic materials can be classified as Hard or Permanent Magnetic materials and Soft Magnetic materials:
Hard or permanent magnetic materials have large size hysteresis loop (obviously hysteresis loss is more) and gradually rising magnetization curve. Ex: carbon steel, tungsten steal, cobalt steel, alnico, hard ferrite etc.
b) Soft magnetic materials have small size hysteresis loop and a steep magnetization curve.
Ex: i) cast iron, cast steel, rolled steel, forged steel etc., (in the solid form).
ii) Silicon steel (Iron + 0.3 to 4.5% silicon) in the laminated form.
c) Special purpose Alloys:
Nickel iron alloys have high permeability and addition of molybdenum or chromium leads to improved magnetic material.
(i) High nickel permalloy (iron +molybdenum +copper or chromium), used in current transformers, magnetic amplifiers etc.,
(ii) Low nickel Permalloy (iron +silicon +chromium or manganese), used in transformers, induction coils, chokes etc.
(iii) Perminvor (iron +nickel +cobalt)
(iv) Pemendur (iron +cobalt +vanadium), used for microphones, oscilloscopes, etc.
(v) Mumetal (Copper + iron)
d) Amorphous alloys (often called metallic glasses):
Amorphous alloys are produced by rapid solidification of the alloy at cooling rates of about a million degrees centigrade per second. The alloys solidify with a glass-like atomic structure which is non-crystalline frozen liquid. The rapid cooling is achieved by causing the molten alloy to flow through an orifice onto a rapidly rotating water cooled drum. This can produce sheets as thin as 10μm and a meter or more wide.

## Slide 9
1
Types of Insulating materials
Solid: Used with field, armature, and transformer windings etc. The examples are:
1) Fibrous or inorganic animal or plant origin, natural or synthetic paper, wood, card board, cotton, jute, silk etc.,
2) Plastic or resins. Natural resins-lac, amber, shellac etc., Synthetic resins-phenol formaldehyde, melamine, polyesters, epoxy, silicon resins, bakelite, Teflon, PVC etc
3) Rubber : natural rubber, synthetic rubber-butadiene, silicone rubber, hypalon, etc.,
4) Mineral : mica, marble, slate, talc chloride etc.,
5) Ceramic : porcelain, steatite, alumina etc.,
6) Glass : soda lime glass, silica glass, lead glass, borosilicate glass
7) Non-resinous : mineral waxes, asphalt, bitumen, chlorinated naphthalene, enamel etc.,
Liquid: Used in transformers, circuit breakers, reactors, rheostats, cables, capacitors etc., & for impregnation. The examples are:
1) Mineral oil (petroleum by product)
2) Synthetic oil askarels, pyranols etc.,
3) Varnish, French polish, lacquer epoxy resin etc.
Gaseous: The examples are:
1) Air used in switches, air condensers, transmission and distribution lines etc.,
2) Nitrogen use in capacitors, HV gas pressure cables etc.,
3) Hydrogen though not used as a dielectric, generally used as a coolant
4) Inert gases neon, argon, mercury and sodium vapors generally used for neon sign lamps.
5) Halogens like fluorine, used under high pressure in cables
No insulating material in practice satisfies all the desirable properties. Therefore a material which satisfies most of the desirable properties must be selected.

## Slide 10
1
Properties Of Insulating Materials
To avoid any electrical activity between parts at different potentials, insulation is used.
An ideal insulating material should possess the following properties.
Should have high dielectric strength.
2) Should with stand high temperature.
3) Should have good thermal conductivity
4) Should not undergo thermal oxidation
5) Should not deteriorate due to higher temperature and repeated heat cycle
6) Should have high value of resistivity ( like 1018 Ωcm)
7) Should not consume any power or should have a low dielectric loss angle δ
8) Should withstand stresses due to centrifugal forces ( as in rotating machines), electro dynamic or mechanical forces ( as in transformers)
9) Should withstand vibration, abrasion, bending
10) Should not absorb moisture
11) Should be flexible and cheap
12) Liquid insulators should not evaporate or volatilize

## Slide 11
1
Types of Insulating materials
Insulating materials can be classified as Solid, Liquid and Gas, and vacuum
Solid: Used with field, armature, transformer windings etc. The examples are:
1) Fibrous or inorganic animal or plant origin, natural or synthetic paper, wood, cotton, jute, silk,rayon, nylon, asbestos, fiber glass
2) Plastic or resins. Natural resins-lac, Synthetic, bakelite, Teflon, PVC
3) Rubber : natural rubber, synthetic rubber, silicone rubber.
4) Mineral : mica, marble.
5) Ceramic
6) Glass
7) Non-resinous : mineral waxes.
Liquid: Used in transformers, circuit breakers, reactors, rheostats, cables, capacitors etc., & for impregnation.
The examples are:
1) Mineral oil
2) Synthetic oil
3) Varnish etc
Gaseous: The examples are:
1) Air used in switches, air condensers, transmission and distribution lines etc.,
2) Nitrogen use in capacitors, HV gas pressure cables etc.,
3) Hydrogen though not used as a dielectric, generally used as a coolant
4) Inert gases neon, argon, mercury and sodium vapors generally used for neon sign lamps.
5) Halogens like fluorine, used under high pressure in cables

## Slide 12: Class of Insulating Material with Thermal considerations
Insulation Class | Max.Operating Temperature | Materials
 | 0C | 
Y | 90 | Cotton , silk, paper, wood, cellulose without oil
A | 105 | Laminated wood, varnished paper , all Y-class material impregnated with natural resin, cellulose esters, insulating oil.
E | 120 | Synthetic resin, Nylon tapes
B | 130 | Mica, glass, fiber, Asbestos
F | 155 | All B- class material with thermal resistance bonding material
H | 180 | Glass fiber, Asbestos, mica with silicon resin
C | >180 | Mica, ceramic, quartz, asbestos with resin of super stability

## Slide 14
1
LECTURE CONTENTS WITH A BLEND OF NPTEL CONTENTS

## Slide 15
1
REFERENCES/BIBLOGRAPHY

## Slide 16
Atul Kulshrestha (Asstt Professor, Electrical Engineering Department) , JECRC, JAIPUR